## Slide 1: Progress Report
Michael Lee
July 20th, 2022

## Slide 2: What was done
Phase recovery code with PyTorch & Holotorch
  Code for generating synthetic WISHED [add citation here] data
  Used PyTorch optimization, NOT Gerchberg-Saxton
    PyTorch optimization converges faster than G.S.
Say something about models
Bug finding

## Slide 3: CONTEXT AND BACKGROUND

## Slide 4: FIRST PROBLEM TO SOLVE
How to recover optical wavefronts?

## Slide 5: Objective
Want to reconstruct optical wavefronts
  I.e. recover amplitude and phase of optical fields
Field has…
Amplitude (arrow length)
and
Phase (oscillation offsets)

## Slide 6: Real Life Setup

## Slide 7: Obtaining Real (Non-Synthetic) Data
Display random phase pattern on SLM
Acquire image from sensor
Save SLM and sensor data
…
Recorded Data
Can use this data in conjunction with a model for SLM-to-sensor propagation to recover the complex field at the image sensor

## Slide 8: Synthetic Data Generator Input
{

## Slide 9: Generating Object Plane Fields
Object itself is not planar
Assumed that phase at object plane was:
Object plane
I am unsure whether or not this is a valid approximation for my particular situation.
Considering ASM, for sufficiently small z and/or when the transverse frequency components are sufficiently bandlimited
However, can get very large, which might mean that even small discrepancies between and can possibly still result in large errors
Could probably use the Huygens-Fresnel principle to calculate the fields on the object plane instead
Seems more computationally intensive though

## Slide 10: Model for Synthetic Data Generation

## Slide 11: Synthetic Data Example

## Slide 12: Recovering Complex Fields
Objective
Recover field (phase + amplitude) at
the image sensor
Can do phase retrieval
to accomplish this
Can focus on SLM and sensor
while disregarding the rest
…
SLM Patterns
and
Sensor Data
Phase Retrieval
Algorithm
Sensor Plane
Complex Fields

## Slide 13: Forward Model
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator

## Slide 14: Recovering Sensor Plane Field
Hypothetical field w/o SLM
Can numerically propagate to obtain
Can assume is the input to the SLMs
SUMMARY
To recover sensor fields:
1. Recover SLM input field
2. Numerically propagate the SLM input field to get the sensor field

## Slide 15: Estimating SLM Input with Optimization
Known/Measured
Sensor Images:
SLM Patterns:
Unknown
SLM Plane Field:
?
Want to find a field that gives approximately the same sensor images
Can use optimization accomplish this

## Slide 16: Optimization Objective Function
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
Minimize error between measured intensity patterns and intensity patterns output by model
CORE IDEA |

## Slide 18
Note phase only SLM
Note that PyTorch/Holotorch works quite well

## Slide 19: Implementation Details

## Slide 20: Stuff to add
Pictures of SLM patterns
Pictures of intensity patterns
Stuff about Gerchberg-Saxton
  I.e. how inverting propagation was done

## Slide 21: Stuff to improve
Readability of labels

## Slide 22: Other
Write for an audience who is not familiar with the work
Specify the problem being solved
  I.e. given intensity patterns from SLMs, recover phase at plane before SLM