## Slide 1: Progress Report
Michael Lee
July 20th, 2022

## Slide 2: What was done
Phase recovery code with PyTorch & Holotorch
  Code for generating synthetic WISHED [add citation here] data
  Used PyTorch optimization, NOT Gerchberg-Saxton
    PyTorch optimization converges faster than G.S.
Say something about models
Bug finding

## Slide 3: CONTEXT AND BACKGROUND

## Slide 4: FIRST PROBLEM TO SOLVE
How to recover optical wavefronts?

## Slide 5: Objective
Want to reconstruct optical wavefronts
  I.e. recover amplitude and phase of optical fields
Field has…
Amplitude (arrow length)
and
Phase (oscillation offsets)

## Slide 6: Why is wavefront recovery difficult?
Why not just sample the fields?
(Like an oscilloscope?)
Optical frequencies: > 400 THz
No ADCs for those frequencies
Use a typical camera sensor?
Standard CCD/CMOS sensors
only capture intensity
Shack-Hartmann wavefront sensor?
Low resolution
Source: Wikimedia
https://commons.wikimedia.org/wiki/File:Shack_Hartmann_WFS_lensletarray.svg
Source: Wikimedia
https://commons.wikimedia.org/wiki/File:Interferometer_Schema.jpg
What about interferometry?
Sensitive to minute movements (e.g. vibration)
Calibration difficulty

## Slide 7: Why is this useful?
Obtaining depth maps of objects
Phase microscopy?

## Slide 8: Phase and Depth
Optical path lengths (OPL) are all equal
(ideal case)
Phase shift over path is proportional to OPL
If the object is sufficiently far away…
However, for ,
is NOT a valid approximation!
Why?
Phase wrapping: )
Small  Small OPL change can drastically affect phase

## Slide 9
Mention that even tiny changes in OPL can lead to big phase differences
Can assume that as object distance gets large, distance between point on object and corresponding point on image converges to the difference in their z-components
Probably cannot assume for phase. Slight changes in image plane location, as well as slight contribution of transverse displacement between point on object and point on image to distance between those points can still have a non-negligible effect.
This arises because wavelength is extremely small. E.g. micrometer shift in image plane location negligible to distance, but non-negligible to phase shift.
Synthetic wavelength holography can help with this as the synthetic wavelengths are larger and thus phase is not as sensitive to small changes in distance.

## Slide 10
Need way to observe effects of phase
Standard camera sensors cannot measure phase
However, SLMs are affected by phase
Can use SLM to get effects of phase to manifest in sensor image

## Slide 11: Basic Setup

## Slide 12: Obtaining Real (Non-Synthetic) Data
Display random phase pattern on SLM
Acquire image from sensor
Save SLM and sensor data
…
Recorded Data
Can use this data in conjunction with a model for SLM-to-sensor propagation to recover the complex field at the image sensor

## Slide 13: Recovering Complex Fields
Objective
Recover field (phase + amplitude) at
the image sensor
Can do phase retrieval
to accomplish this
Can focus on SLM and sensor
while disregarding the rest
…
SLM Patterns
and
Sensor Data
Phase Retrieval
Algorithm
Sensor Plane
Complex Fields

## Slide 14: Forward Model
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator

## Slide 15: Recovering Sensor Plane Field (Part 1)
Suppose one knew the

## Slide 16: Estimating SLM Input with Optimization
Known/Measured
Sensor Images:
SLM Patterns:
Unknown
SLM Plane Field:
?
Want to find a field that gives approximately the same sensor images

## Slide 17: Optimization Objective Function
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
Minimize (mean-)squared error between measured intensity patterns and intensity patterns output by model
CORE IDEA |

## Slide 19: Synthetic Data Example

## Slide 20
Note phase only SLM
Note that PyTorch/Holotorch works quite well
Mention assumption that the field at the SLM plane when there is no SLM present would be the same field that gets “input” to the SLM

## Slide 21: Implementation Details

## Slide 23: Stuff to add
Pictures of SLM patterns
Pictures of intensity patterns
Stuff about Gerchberg-Saxton
  I.e. how inverting propagation was done

## Slide 24: Stuff to improve
Readability of labels

## Slide 25: Other
Write for an audience who is not familiar with the work
Specify the problem being solved
  I.e. given intensity patterns from SLMs, recover phase at plane before SLM