## Slide 1: REPORT
Michael Lee
October 6th, 2022

## Slide 2: What was accomplished

## Slide 3: WISHED/Phase Recovery
Code for generating synthetic WISHED data
  Has a model-based and some non-model-based modes
WISHED processing code
  Phase recovery code
    Model-based, uses SLM patterns and image sensor data
    NOTE: I did not get around to implementing a PyTorch Lightning module for the optimization.
  Synthetic wavelength code
    I.e. pointwise-multiplying fields together (with one being complex-conjugated)
  Depth recovery code
    NOTE: My depth recovery code has/might have some flaws, as explained later. At the very least, I forgot to do phase unwrapping.
NOTE: All code was written using PyTorch and Holotorch.

## Slide 4: Holotorch Stuff
Documented bugs in Holotorch that I encountered
Wrote code to fix/work around bugs when needed
  Did so without modifying Holotorch source code itself
    (Good thing Python supports inheritance)
Implemented new classes in Holotorch
  Thin lens component
  Field padder/unpadder
  Field resampler
  Et cetera

## Slide 5: DETAILS

## Slide 6: Real Life Setup and General Objective
OBJECTIVE
Recover the complex field (amplitude and phase) on the image sensor plane (without the SLM)
Use the recovered phase to obtain the depthmap of the object.
NOTE: Phase-only SLM

## Slide 7: Obtaining Real (Non-Synthetic) Data
Display random phase pattern on SLM
Acquire image from sensor
Save SLM and sensor data
…
Recorded Data
Can use this data in conjunction with a model for SLM-to-sensor propagation to recover the complex field at the image sensor

## Slide 8: Generating Synthetic Data
SYSTEM MODEL
. . .
Specify a ground truth depthmap
via an image
Specify a model for the system
Use depth map to
generate object plane
fields
Feed the calculated object plane fields into the system
Can simulate the real-life WISHED data collection process.
Sensor plane and SLM images are saved.
NOTE
Synthetic data code has some modes/options (e.g. ray optics) that do not utilize a model like this.

## Slide 9: Computing Object Plane Field from Depthmap
Object itself is not planar
Assumed that phase at “object plane” was proportional to depth:
I am not sure if this approximation is valid
  Might not be valid for small wavelengths?
  Might be more valid for larger (synthetic or non-synthetic) wavelengths?
  Might be valid if only very paraxial/sufficiently paraxial rays are considered????????
Using the Huygens-Fresnel principle might be more accurate?
  The integral seems more computationally intensive to compute though
  I wrote some code for this in MATLAB, but it is slow
    It was vectorized and utilized the GPU
    However, I had to break the integral up into pieces so as not to run out of GPU memory
Object plane

## Slide 10: Synthetic Data System Model
ASM
Propagation
Thin Lens
Fresnel
Two-Step
Propagator
Distance = 50cm
Focal Length = 75mm
Diameter = 50.8mm
Distance 88.2mm
Sensor
Object Plane
Field
Sensor Plane
Field
Fresnel Two-Step Propagator
"Computational Fourier Optics: A MATLAB Tutorial“
by David Voelz
Follows setup from 2020 WISHED paper
The Fresnel two-step propagator was used to propagate between planes of different resolutions. It was used because the image on the image plane is comparatively small relative to the object plane fields.
Sensor is placed at the image plane.

## Slide 11: Synthetic Data System Model Fields
Ran into some GPU memory and numerical/computational issues (the latter mainly arising from the Fresnel two-step propagator).
Thus, was unable to get the image on the sensor plane to be bigger.
Field at sensor plane

## Slide 12: Visualizing the Test Object
NOTE: The 3D model was not used for computations.
It is a just a visualization of the depthmap.

## Slide 13: Synthetic Data Example

## Slide 14: Recovering Complex Fields
Objective
Recover field (phase + amplitude) at
the image sensor
Can do phase retrieval
to accomplish this
Can focus on SLM and sensor
while disregarding the rest
…
SLM Patterns
and
Sensor Data
Phase Retrieval
Algorithm
Sensor Plane
Complex Fields
]
This data is measured
(or synthesized)

## Slide 15: Forward Model
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator

## Slide 16: Recovering Sensor Plane Field
Hypothetical field w/o SLM
Can numerically propagate to obtain
Can assume is the input to the SLMs
SUMMARY
To recover sensor fields:
1. Recover SLM input field
2. Numerically propagate the SLM input field to get the sensor field

## Slide 17: Estimating SLM Input with Optimization
Known/Measured
Sensor Images:
SLM Patterns:
Unknown
SLM Plane Field:
?
Want to find a field that gives approximately the same sensor images
Can use optimization accomplish this

## Slide 18: Optimization Objective Function
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
Minimize error between measured intensity patterns and intensity patterns output by model
CORE IDEA |
My actual implementation does something similar to batch gradient descent (batch ADAM???). Not all samples are evaluated at once like the equation above implies.
NOTE:

## Slide 19: Recovered Sensor Plane Fields
Numerical artifact
Many discontinuities
Infeasible to unwrap
No difficult discontinuities
Phase related to depth
Aliasing?

## Slide 20: Depth Recovery Implementation Assumptions
Phase wrapping: )
Small  Small OPL change can drastically affect phase
If the object is sufficiently far away…
Assuming free space, disregarding lens thickness, ignoring slight changes in image plane location due to changing points having different z coordinates, ignoring lens imperfections
The code ASSUMES that the phase at the image sensor is proportional to distance in z-direction.
This seems like for small , this could be a bad approximation in certain cases.
I assumed it would be okay for larger synthetic wavelengths, but I am unsure if my assumption was correct.
[
Sensor plane phase
term gets very large for small so if the distance approximation is even just m off, the approximation might not be good for predicting the sensor plane phase or object depth.

## Slide 21: Recovered Depthmaps from Synthetic Data
Median filter
(To remove spikes)
Gaussian filter
(See 2020 WISHED paper)

## Slide 22: Recovered Depthmaps (3D Visualization)

## Slide 23: Caveats for depth recovery implementation/results
I overlooked some details in the 2020 WISHED paper
  Did not use two synthetic wavelengths for unwrapping
  Did not recover fields at object plane
    I was not able to figure out if it was necessary to do so or not
    Section 4.1 of the 2020 WISHED paper mentions recovering the object plane fields though
I am not sure if my synthetic data was valid
  Unsure if object plane fields were valid or not (see earlier slide)
  Numerical artifacts in synthetic data generation
I am unsure if my underlying assumptions about how sensor plane phase corresponds to depth were correct.

## Slide 24: Additional Note on Depth Recovery Results
Used a synthetic wavelength that was larger than the simulated object’s depth variation (~6mm versus 1mm respectively)
  phase fits within 0 to 2
Did not do any sort of phase unwrapping in implementation
Phases were recentered around zero
  Specifically, some quick optimization was performed to find the constant/absolute phase shift that minimized the variance about zero of the resulting phases.
    Which, now that I think about it, I think that would be equivalent to just phase shifting everything so that the mean phase was zero.
      Oops.

## Slide 25: END OF SLIDES