## Slide 1: MODEL-BASED INVERSION
Michael Lee
November 29th, 2022

## Slide 2: Inverse Problems
What is an inverse problem?

## Slide 3: What is an Inverse Problem?
Given a set of observations, find the causes
Example – Inverse scattering
IMAGE SOURCE: Figure 1 from “Time reversal techniques in ultrasonic nondestructive testing of scattering media” by Prada et al
Given
Reflected signals from scatterer(s)
(observations)
Find
The location of the scatterer(s)
(causes)
Applications of Inverse Scattering
— Medical imaging (ultrasound)
— Fault detection
— Ground-penetrating radar

## Slide 4: An Abstract View
Model Parameters
()
Forward Operator
(Measurement Operator)
Data/Measurements
()
Examples of Model Parameters
— Scatterer locations
— Electric field amplitudes/phases
— Depth map of a surface
Examples of Data/Measurements
— Scattered signal waveforms
— Camera sensor measurements
— Phases from interferometry
SOURCE: [1] – Introduction to Inverse Problems, by Guillame Bal
– Space of model parameters
– Space of data/measurements
Additional Information
— is a mapping (i.e. function)
— Ideally invertible (injective) but not always
Maps model parameters to measurements

## Slide 5: The Problem
How to measure heights/depths over a 3D surface?
Notes: An example of an inverse problem is figuring out the shape of a 3D surface using images taken by a standard camera sensor---like, a charge coupled device or a CMOS image sensor.
[next slide]

## Slide 6: DEPTHMAPS
Depthmaps encode 3D surfaces as depths (or heights)
IMAGE SOURCE: Figure 4 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al
Notes: To give a more visual representation, here is a depthmap.
Depthmaps encode 3D surfaces as depths or heights
So they are kinda like a topographic map of a terrain
Each point on a topographic map has a height
Similarly, one can represent a 3D surface as a series of depths or heights

## Slide 7: Interpreting Depthmaps
Notes: So how does one interpret depthmaps?
Well, they are presented as a 2D plot where color represents height
If you look at the upper right segment, the depth is about 1mm and that segment is higher than the rest
This can be seen in the 3D models to the left

## Slide 8: The Approach
Using phase to determine distance
Notes: So how does one obtain a depthmap?
Well, there are a number of methods.
One could use a time-of-flight measurement.
Or maybe a ruler.
Or perhaps some sort of phase measurement, like in optical coherence tomography.
The specific approach taken by the papers I will be presenting on involve using phase to determine distance or depth.

## Slide 9: Recovering Depth from Phase
Ideal thin lens  Same-colored lines have the same optical path length (OPL)
Sufficiently large , 
Can theoretically get depth from the phases at the sensor plane
Phase shift between points is PROPORTIONAL to optical path length!
How does this relate to depth?
If the object is far enough away….
Optical path length axial distance/distance in the z-direction
HOWEVER small complicates matters.
Notes: First some optics
Does anyone know the definition of optical path length?
…
Good! But in this case, since most of this system is air, OPL is pretty much equal to the distance a light ray travels.
(Of course, lens has thickness; can use thin lens approx. and disregard)
All rays coming from point imaged to same point
OPL same for all paths
OPL essentially distance between point on object and point on image
Phase shift prop. to OPL so everything in-phase
---
Troubles with small wavelengths:
Lateral shifts cause phase shifts so phase does not perfectly correspond to depth, lens imperfections, the fact that image plane slightly shifts with differing depth, etc

## Slide 10: Challenge – Shifting Image Plane
Ray optics
Points in the object plane get focused onto the image plane
What about non-planar objects?
Image plane shifts (slightly)!
But there are even bigger problems than that…

## Slide 11: Challenge – Lateral Shifts
Units: mm
Units: mm
OPL difference
 Small, right?
Not compared to an optical wavelength!
At , !
Phase difference between paths !

## Slide 12: Challenge – Lateral Shifts
Notes: Here is a visual
Rings due to lateral shifts

## Slide 13: Challenge – Phase Wrapping
Phase shift periodic with period
A given phase corresponds to multiple OPLs, making OPL/distance ambiguous
corresponds to OPLs
usually small  depth range severely limited (without unwrapping, etc)
Example: Cannot tell the difference between distances and

## Slide 14: Challenge – Surface Roughness
Surface roughness causes issues
   phase fluctuates wildly
  Phase distribution looks like noise

## Slide 15: Challenges – Summary
Depth ambiguity
  Multiple distances can correspond to the same phase
Path length/phase variations
  Object roughness  Path length variations  Wild phase variations
  Lateral shifts
  Shifting image plane

## Slide 16: Fields and Phases
Notes: So, now that I have hopefully killed your dreams of using phase to recover depth, let’s learn about fields and phases!
(Deadpan) In all seriousness, the aforementioned problems are addressed later.
Anyways, let’s start with some visuals.

## Slide 17: Electric Fields and Phase
Light = Electromagnetic wave
(at least below ultraviolet)
Monochromatic light  Electric field oscillates at a fixed frequency
Fields oscillate in a periodic
pattern/shape
 Phasor representation
Notes: In optics, we measure light
Light is an electromagnetic wave, at least up to the visible range
Once we start getting up into the ultraviolet range, light starts behaving more like a particle
But we are focusing on visible wavelengths and longer
[advance in slide]
Now, since light is an electromagnetic wave, it has a corresponding electric field
For monochromatic light---i.e. single wavelength or single frequency light---the electric field will oscillate in a periodic fashion.
For example, the field could oscillate linearly, like the linearly polarized field on the left.
[advance in slide]
Or one could have circular polarization, like the field on the right.
Regardless, for monochromatic light, the field at each point oscillates in a pattern.
The patterns are not necessarily uniform across all points, but they all have the same period in time.
Some points might “lag” behind others---in other words, there are phase offsets.
The electric field amplitude can vary from point to point as well.
[brief pause]
So, each point in the electric field has an amplitude and a phase offset associated with it.
Mathematically, the fact that every point oscillates at the same frequency allows us to separate this amplitude and phase from the oscillating-in-time part of the field.
The amplitudes and phases of oscillating waves can be expressed as phasors: complex numbers that have a magnitude and a phase.
In this presentation, we will primarily be working in the phasor domain.
[advance in slide]
[brief pause]
It should be noted though that electric fields are vector fields, so there is a phasor for each component---x, y, and z.
However, for the purposes of this presentation, we can ignore that.
[next slide]
-----------------------
(Ex(x,y,z; t=t0) a_x, Ey(x,y,z; t=t0) a_y, Ez(x,y,z; t=t0) a_z) e^{-jwt}  can have e^{+jwt} depending on convention

## Slide 18: Measuring Phase

## Slide 19: If this were RF/Microwaves…
Can sample signals in time
  Oscilloscopes, A/D converters
  Sampling rate Measured bandwidth
Could demodulate
  I/Q demodulation  could recover phasors

## Slide 20: In optics-land…
Direct sampling
  Frequencies in 100’s of THz
  No current devices can sample fast enough
Demodulation?
  Would need a suitable optical demixer/demodulator
Interferometry?
  Yes, but…
Notes: Sampling
Massive bandwidth needed
Not sure how developed optical mixing technology is
Would almost certainly be less developed than RF/microwave mixers
Instead of demod, perhaps interferometry could be used

## Slide 21: Interferometry
IMAGE SOURCE: https://commons.wikimedia.org/wiki/File:Michelson_interferometer_fringe_formation.svg
Phase recovered by observing interference patterns
Small wavelengths  Small disturbances can interfere with measurements
Mismatched sample & reference beam power
 Contrast in interference pattern reduces
Powerful technique, but…

## Slide 22: Shack-Hartmann Wavefront Sensor
IMAGE SOURCE: https://commons.wikimedia.org/wiki/File:Shack_Hartmann_WFS_lensletarray.svg
Notes: Another way is SHWS
Lenslet array placed one focal length away from image sensor
Thus FT relationship
Wavefront phase gradient gets FT’d to a point
Limited resolution due to lenslets
Interference between lenses

## Slide 23: Phase recovery/Retrieval
Leveraging computational optics to recover phase
Notes: So existing methods have some limitations
We live in computer age though
Why not use computers
Can use comp optics to get good phase recovery results

## Slide 24: Phase Retrieval Problem
Monochromatic light wavefront
Imagine (monochromatic) light shining on
a camera sensor
Electric field at each point in space has
a magnitude and a phase
Field has a magnitude and a phase at each point
Electric field at sensor plane
Standard camera sensors can only measure intensity
Problem
How does one recover amplitude and phase?

## Slide 25: Phase Retrieval Problem – Formal Statement
SOURCE: [5]
GIVEN: A measurement 𝒚
FIND: Corresponding parameters
WHERE
ℳ{}
is a linear transformation
KNOWN
ℳ{}
Model Parameters
()
Forward Operator
(Measurement Operator)
Data/Measurements
()
– Space of model parameters
– Space of data/measurements
Plane you wish to
recover fields for
Plane where you measured intensity
Operator describing
propagation + absolute value
Notes: But b4 we move on, let’s formalize the phase retrieval problem

## Slide 26: Phase Retrieval Methods
Convex relaxations
Approximate message passing
Alternating projection methods
  Gerchberg-Saxton
The run-a-model-in-PyTorch-with-autograd-and-do-gradient-descent method
SOURCE: [5]

## Slide 27: Gerchberg-Saxton Algorithm
KNOWN
Intensity measurement at source plane
Intensity measurement at target plane
Propagation & inverse propagation operators
SOURCES: [2], [6]
Propagate
Invert Propagation
Constrain Amplitude
Constrain Amplitude
Target Plane
Source Plane
Notes: There are a number of variations on the Gerchberg-Saxton algorithm.
Does not exactly follow the formal definition for phase retrieval that was described earlier.
Oftentimes have a Fourier transform lens setup so propagation can be modeled by FTs

## Slide 28: WISH: Wavefront Imaging Sensor with High Resolution
Obtaining wavefront phases using computational phase retrieval
For more information on WISH, see [3].
Notes: So how can we use comp. phase retr. in actual system?
Well paper w/in past decade described just that

## Slide 29: WISH(ED) Setup and General Objective
OBJECTIVE
Recover the complex field (amplitude and phase) on the image sensor plane (without the SLM)
Use the recovered phase to obtain the depthmap of the object.
NOTE: Phase-only SLM
SOURCES: [2], [3]
Notes: DESCRIBE SLM

## Slide 30: Obtaining Data
Display random phase pattern on SLM
Acquire image from sensor
Save SLM and sensor data
…
Recorded Data
Can use this data in conjunction with a model for SLM-to-sensor propagation to recover the complex field at the image sensor
SOURCE: [2]

## Slide 31: Recovering Complex Fields
Objective
Recover field (phase + amplitude) at
the image sensor
Can do phase retrieval
to accomplish this
Can focus on SLM and sensor
while disregarding the rest
…
SLM Patterns
and
Sensor Data
Phase Retrieval
Algorithm
Sensor Plane
Complex Fields
]
This data is known/measured
SOURCE: [2]

## Slide 32: Forward Model
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
NOTE: There are other ways of modeling propagation besides ASM (angular spectrum method).

## Slide 33: Recovering Sensor Plane Field
Hypothetical field w/o SLM
Can numerically propagate to obtain
Can assume is the input to the SLM
SUMMARY
To recover sensor fields:
1. Recover SLM input field
2. Numerically propagate the SLM input field to get the sensor field
SOURCE: [2]

## Slide 34: Estimating SLM Input with Optimization
Known/Measured
Sensor Images:
SLM Patterns:
Unknown
SLM Plane Field:
?
Want to find a field that gives approximately the same sensor images
Can use optimization accomplish this
SOURCE: [2]

## Slide 35: Optimization Objective Function
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
Minimize error between measured intensity patterns and intensity patterns output by model
CORE IDEA |
NOTE: Other propagation operators besides ASM can also be used.
SOURCE: [2]
Notes: Methods for phase recovery:
Gerchberg-Saxton
Minimizing objective function
  System model + PyTorch autograd

## Slide 36: Phase Recovery Results (Single Wavelength)
IMAGE SOURCE: Figure 5 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al
Small  Wrapped phases
Wrapped phases are bad for depth recovery
Notes: WISH was designed for pretty small scales
Aforementioned lateral phase shifting problem present here
Transmissive analogous to depth

## Slide 37: Synthetic Wavelengths
Multiplying fields at two different wavelengths to get a longer, synthetic wavelength
Notes: Turns out earlier problems can be mitigated with synth wavelengths

## Slide 38: First Example – Separate Wavelengths
Wavelength 1
Wavelength 2
Notes: Here is example
Two separate wavelengths

## Slide 39: First Example – Obtaining Synthetic Wavelengths
conj
“conj“ means (pointwise) complex conjugation
X
Pointwise multiplication

## Slide 40: First Example – Both Wavelengths
Synthetic Wavelength
Wavelengths (Superimposed)

## Slide 41: Second Example – Separate Wavelengths
Wavelength 2
Wavelength 1
Notes: Now what would this look like on image sensor?

## Slide 42: Second Example – Obtaining Synthetic Wavelengths
conj
“conj“ means (pointwise) complex conjugation
X
Pointwise multiplication

## Slide 43: Second Example – Both Wavelengths
Synthetic Wavelength
Wavelengths (Superimposed)

## Slide 44: Synthetic Wavelengths
Big picture
Can correlate (“multiply”) two complex fields of nearby wavelengths together to get a larger, synthetic wavelength.
Synthetic wavelength
(𝛬)
Height/depth
SOURCE: [2]

## Slide 45: Synthetic Wavelength Math
Fields:
Synthetic fields:
 | i-th wavelength
 | Complex (phasor) field incident on the sensor for
 | Amplitude of the field incident on the sensor for
 | Optical path length corresponding to the point for
 | Distance associated with each point . NOTE:
 | i-th wavelength
Synthetic wavelength
Notes: Here is some math

## Slide 46: WISHED: Wavefront Imaging Sensor with High Resolution AND DEPTH RANGING
Improving unambiguous depth range using synthetic wavelengths
For more information on WISHED, see [2].
Notes: WISHED makes use of synth wavelengths

## Slide 47: How WISHED Uses Synthetic Wavelengths
Better unambiguous range
   wrapped phase for spans larger length
  Can combine with an even larger synthetic wavelength to help further unwrap
Less susceptible to path length variations
  Less affected by surface roughness
SOURCE: [2]

## Slide 48
IMAGE SOURCES: Figures 5 and 12 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al

## Slide 49: Demo with Synthetic Data*
Done with Python/PyTorch with the Holotorch library [4]
*Of questionable quality/validity.
Notes: I will be uploading my code and slides later
The reason why I say questionable is because I modeled depth as just a phase shift proportional to displacement along z-direction
Okay approximation---if rays are VERY paraxial

## Slide 50: Visualizing the Test Object
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 51: Recovered Sensor Plane Fields
Many discontinuities
Infeasible to unwrap phase
No difficult discontinuities
Phase related to depth
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 52: Recovered Depthmaps from Synthetic Data
Median filter
(To remove spikes)
Gaussian filter
(See 2020 WISHED paper)
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 53: Recovered Depthmaps (3D Visualization)
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 54: References
[1] G. Bal, Introduction to Inverse Problems. 2019.
https://www.stat.uchicago.edu/~guillaumebal/PAPERS/IntroductionInverseProblems.pdf.
[2] Y. Wu, F. Li, F. Willomitzer, A. Veeraraghavan, and O. Cossairt, “WISHED: Wavefront imaging
sensor with high resolution and depth ranging,” 2020 IEEE International Conference on
Computational Photography (ICCP), 2020.
[3] Y. Wu, M. K. Sharma, and A. Veeraraghavan, “WISH: Wavefront imaging sensor with high
resolution,” Light: Science & Applications, vol. 8, no. 1, 2019.
[4] Facebookresearch, “Facebookresearch/holotorch: Holotorch is an optimization framework for
differentiable wave-propagation written in PyTorch,” GitHub. [Online]. Available: https://github.com/facebookresearch/holotorch. [Accessed: 21-Nov-2022].
[5] C. A. Metzler, M. K. Sharma, S. Nagesh, R. G. Baraniuk, O. Cossairt, and A. Veeraraghavan, “Coherent inverse scattering via transmission matrices: Efficient Phase Retrieval Algorithms and a public dataset,” 2017 IEEE International Conference on Computational Photography (ICCP), 2017.
[6] “Gerchberg–Saxton algorithm,” Wikipedia, 12-Jul-2022. [Online]. Available:
https://en.wikipedia.org/wiki/Gerchberg%E2%80%93Saxton_algorithm.