## Slide 1: MODEL-BASED INVERSION
Michael Lee
October 6th, 2022

## Slide 2: Inverse Problems
What is an inverse problem?

## Slide 3: What is an Inverse Problem?
Given a set of observations, find the causes
Example – Inverse scattering
IMAGE SOURCE: Figure 1 from “Time reversal techniques in ultrasonic nondestructive testing of scattering media” by Prada et al
Given
Reflected signals from scatterer(s)
(observations)
Find
The location of the scatterer(s)
(causes)
Applications of Inverse Scattering
— Medical imaging (ultrasound)
— Fault detection
— Ground-penetrating radar

## Slide 4: An Abstract View
Model Parameters
()
Forward Operator
(Measurement Operator)
Data/Measurements
()
Examples of Model Parameters
— Scatterer locations
— Electric field amplitudes/phases
— Depth map of a surface
Examples of Data/Measurements
— Scattered signal waveforms
— Camera sensor measurements
— Phases from interferometry
SOURCE: [1] – Introduction to Inverse Problems, by Guillame Bal
– Space of model parameters
– Space of data/measurements
Additional Information
— is a mapping (i.e. function)
— Ideally invertible (injective) but not always
Maps model parameters to measurements

## Slide 5: The Problem
How to heights/depths on a 3D surface?

## Slide 6: DEPTHMAPS
Depthmaps encode 3D surfaces as depths (or heights)
IMAGE SOURCE: Figure 4 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al

## Slide 7: Recovering Depth from Phase
Lens  Same-colored lines have the same optical path length (OPL)
Sufficiently large , 
Can theoretically get depth from the phases at the sensor plane,
but small complicates matters.
Notes: Troubles with small wavelengths:
Lateral shifts cause phase shifts so phase does not perfectly correspond to depth, lens imperfections, the fact that image plane slightly shifts with differing depth, etc

## Slide 8: Phase Retrieval Problem
Monochromatic light wavefront
Imagine (monochromatic) light shining on
a camera sensor
Electric field at each point in space has
a magnitude and a phase
Field has a magnitude and a phase at each point
Electric field at sensor plane
Standard camera sensors can only measure intensity
Problem
How does one recover amplitude and phase?

## Slide 9: WISH: Wavefront Imaging Sensor with High Resolution
Obtaining wavefront phases using computational phase retrieval
For more information on WISH, see [3].

## Slide 10: WISH(ED) Setup and General Objective
OBJECTIVE
Recover the complex field (amplitude and phase) on the image sensor plane (without the SLM)
Use the recovered phase to obtain the depthmap of the object.
NOTE: Phase-only SLM
SOURCES: [2], [3]

## Slide 11: Obtaining Data
Display random phase pattern on SLM
Acquire image from sensor
Save SLM and sensor data
…
Recorded Data
Can use this data in conjunction with a model for SLM-to-sensor propagation to recover the complex field at the image sensor
SOURCE: [2]

## Slide 12: Recovering Complex Fields
Objective
Recover field (phase + amplitude) at
the image sensor
Can do phase retrieval
to accomplish this
Can focus on SLM and sensor
while disregarding the rest
…
SLM Patterns
and
Sensor Data
Phase Retrieval
Algorithm
Sensor Plane
Complex Fields
]
This data is known/measured
SOURCE: [2]

## Slide 13: Forward Model
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
 | Complex field incident on SLM
 | Pointwise phase shift applied by SLM
 | ASM propagation operator
NOTE: There are other ways of modeling propagation besides ASM (angular spectrum method).

## Slide 14: Recovering Sensor Plane Field
Hypothetical field w/o SLM
Can numerically propagate to obtain
Can assume is the input to the SLM
SUMMARY
To recover sensor fields:
1. Recover SLM input field
2. Numerically propagate the SLM input field to get the sensor field
SOURCE: [2]

## Slide 15: Estimating SLM Input with Optimization
Known/Measured
Sensor Images:
SLM Patterns:
Unknown
SLM Plane Field:
?
Want to find a field that gives approximately the same sensor images
Can use optimization accomplish this
SOURCE: [2]

## Slide 16: Optimization Objective Function
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
 | Estimated complex field incident on SLM
 | Complex field incident on SLM
 | Pointwise phase shift applied by ith SLM pattern
 | Intensity pattern on sensor due to ith SLM pattern
 | ASM propagation operator
Minimize error between measured intensity patterns and intensity patterns output by model
CORE IDEA |
NOTE: Other propagation operators besides ASM can also be used.
SOURCE: [2]
Notes: Methods for phase recovery:
Gerchberg-Saxton
Minimizing objective function
  System model + PyTorch autograd

## Slide 17: Phase Recovery Results (Single Wavelength)
IMAGE SOURCE: Figure 5 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al
Small  Wrapped phases
Wrapped phases are bad for depth recovery

## Slide 18: WISHED: Wavefront Imaging Sensor with High Resolution AND DEPTH RANGING
Improving unambiguous depth range using wavelength diversity
For more information on WISHED, see [2].

## Slide 19: Issues with Small Wavelengths
Depth ambiguity
  Phase wrapped to or , corresponds to a range of
Object roughness  Path length variations
Lateral shifts can affect phase (not just depth shifts)
???  Image plane location depends on , variation might be

## Slide 20: Synthetic Wavelengths
Big picture
Can correlate (“multiply”) two complex fields of nearby wavelengths together to get a larger, synthetic wavelength.
Synthetic wavelength
(𝛬)
Height/depth
SOURCE: [2]

## Slide 21: Advantages of Synthetic Wavelengths
Better unambiguous range
   wrapped phase for spans larger length
  Can combine with an even larger synthetic wavelength to help further unwrap
Less susceptible to path length variations
  Less affected by surface roughness
SOURCE: [2]

## Slide 22
IMAGE SOURCES: Figures 5 and 12 from [2] – “WISHED: Wavefront imaging sensor with high resolution and depth ranging” by Wu et al

## Slide 23: Demo with Synthetic Data*
Done with Python/PyTorch with the Holotorch library [4]
*Of questionable quality/validity.

## Slide 24: Visualizing the Test Object
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 25: Recovered Sensor Plane Fields
Many discontinuities
Infeasible to unwrap phase
No difficult discontinuities
Phase related to depth
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 26: Recovered Depthmaps from Synthetic Data
Median filter
(To remove spikes)
Gaussian filter
(See 2020 WISHED paper)
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 27: Recovered Depthmaps (3D Visualization)
NOTE: This is synthetic data, shown for illustrative purposes.

## Slide 28: References
[1] G. Bal, Introduction to Inverse Problems. 2019.
https://www.stat.uchicago.edu/~guillaumebal/PAPERS/IntroductionInverseProblems.pdf.
[2] Y. Wu, F. Li, F. Willomitzer, A. Veeraraghavan, and O. Cossairt, “WISHED: Wavefront imaging
sensor with high resolution and depth ranging,” 2020 IEEE International Conference on
Computational Photography (ICCP), 2020.
[3] Y. Wu, M. K. Sharma, and A. Veeraraghavan, “WISH: Wavefront imaging sensor with high
resolution,” Light: Science & Applications, vol. 8, no. 1, 2019.
[4] Facebookresearch, “Facebookresearch/holotorch: Holotorch is an optimization framework for
differentiable wave-propagation written in PyTorch,” GitHub. [Online]. Available: https://github.com/facebookresearch/holotorch. [Accessed: 21-Nov-2022].